## Slide 1: Produced Water Facility Emissions

## Slide 2: UDAQ Emission Methodology
Monthly samples are collected at facilities
Throughput data is gathered by U.D.O.G.M.
Emissions = Facility Throughput * Emission Factor
  Emission Factor is derived from monthly water samples
    2014 emission factor was derived from a single sample event in December of 2016
      4 facilities evaporation pond samples were averaged together
      Only 1 facility operated and sampled a skim pond
    Future emission factor will be derived from an average of all months of sampling

## Slide 3: Emission Factor Assumptions
All of Gasoline Range Organics (GRO: C6-C12) is evaporated
50% of Diesel Range Organics (DRO: C10-C28) is evaporated
  The other 50% are assumed to be degraded or drop out as sludge
A facilities throughput first goes through the skim pond then through the evaporation pond (Both emission factors apply)

## Slide 4: Samples and Data
Companies A – D sample is after gravity and mechanical separation at outfall to first open water source (no skim ponds)
Company E uses open top gravity separation and skim ponds
 | Methanol (mg/L) | VOC |  | Benzene (mg/L) | Toluene (mg/L) | Ethylbenzne (mg/L) | Total Xylene (mg/L)
 |  | *GRO (mg/L) | *DRO (mg/L) |  |  |  | 
Company A | 278 | 150 | 220 | 25.21 | 46.06 | 2.60 | 32.61
Company B | 696 | 84.5 | 623 | 6.82 | 21.10 | 1.29 | 17.10
Company C | 1500 | 39.8 | 740 | 11.00 | 12.00 | 0.44 | 5.97
Company D | 3.2 | 21 | 17.2 | 6.82 | 6.08 | 0.29 | 3.67
Company E | 51 | 26000 | 26 | 228.20 | 748.10 | 109.88 | 330.00
*GRO (C6-C12)
*DRO (C10-C28)

## Slide 5: UDAQ Basin Emission Inventory Results
Total Throughput (in barrels) in the Basin as reported to UDOGM in 2014 | 
11,472,505.00 | Commercial
4,195,080.00 | Non-Commercial
15,667,585.00 | Total
Emission Totals | 
1,301.15 | Tons from Evaporation Ponds
71,461.40 | Tons from Skim Ponds
72,762.55 | Total Tons from Produced Water facilities
Operator | Methanol (lb/bbl) | VOC (lb/bbl) | Benzene (lb/bbl) | Toluene (lb/bbl) | Ethylbenzne (lb/bbl) | Total Xylene (lb/bbl) | 
Company A | 0.097 | 0.130 | 0.009 | 0.016 | 0.001 | 0.011 | 
Company B | 0.244 | 0.248 | 0.002 | 0.007 | 0.000 | 0.006 | 
Company C | 0.526 | 0.273 | 0.004 | 0.004 | 0.000 | 0.002 | 
Company D | - | 0.013 | 0.002 | 0.002 | 0.000 | 0.001 | 
AVERAGE | 0.289 | 0.166 | 0.004 | 0.007 | 0.000 | 0.005 | EVAP PONDS
Company E |  | 9.122 | 0.080 | 0.262 | 0.039 | 0.476 | SKIM PONDS

## Slide 6: All Facilities not created equal
Company E
  Separation in open top concrete vault
  Skim Ponds
  Uncontrolled VOC emissions from ponds alone ~ 6,000 tons (using sources samples)
Company D
  Separation done in tanks and centrifuges
  No Skim Ponds
  Uncontrolled VOC emissions from ponds alone ~ 375 tons (using sources samples)

## Slide 7: Over Assumptions 2014
Majority of Produced water facilities are uncontrolled (assume all on Indian Land are)
Uncontrolled PTE emissions range from 175 – 6,000 tons of VOCs per year per facility (from 6 facilities)
Average Uncontrolled PTE’s for facility on state land ~1,350 tpy
  6 facilities (one has no ponds still 175 tons) = ~ 8,200 tons per year
Do the over assumptions help capture the other equipment we didn’t collect info for?

## Slide 8: Moving Forward
Emission Factor needs refining
  Is all GRO evaporating, is some degrading?
    Need to account for oil skimmed off, its not evaporating
  Sludge accumulation, is this all DRO?
Skim Pond Factor
  Seasonal effects?
Skim Pond Emission Factor |  | 
9.122 | Collected in December of 2016 | 
1.467 | Collected in May of 2017 | 
5.294 | Average | 

## Slide 9: Emissions Sources
Storage Tanks
Evap Ponds
Centrifuges
Landfarm
Landfill
Engines
Combustors
Main VOC Sources

## Slide 10: Uncontrolled Facility Example
~1,000 ton VOC Facility
  VOC Emissions by Source (Uncontrolled*)
    Tanks account for ~30%
    Ponds account for ~38%
    Landfarm and Landfill ~30%
    Loading, engines, etc. ~2%
*Assume in 2014 all facilities were uncontrolled

## Slide 11: Same Facility Controlled
190 ton VOC Facility
  Skim ponds removed voluntarily
  VOC Emissions by Source (Controlled)
    Tanks account for ~5%
    Ponds account for ~55%
    Landfarm and Landfill ~33%
    Loading, engines, etc. ~7%

## Slide 12: Questions
?