## Slide 1
Produced Water Emissions Research Summary
Marc Mansfield, Huy Tran, and Seth Lyman

## Slide 2
Measurement Techniques:
Flux Chamber
Fused silica-lined canisters
for C2-C11 hydrocarbons
Control/measurement of flow, pressure, temp
Acrylic floating flux chamber
Cavity ring-down CH4/CO2/H2O analyzer
(Concin – Concout)
Surface area
Flux = × Flow Rate
~225 hour-long measurements in Uinta Basin and Wyoming at 10 facilities (facilities in Basin account for 25% of total Basin pond area)
Evidence exists that chamber is biased low in high winds. More about this later
Notes: 2

## Slide 3
Water Composition
Notes: 3

## Slide 4
Emission Flux Composition
Notes: 4

## Slide 5
Emission Flux Composition
Notes: 5

## Slide 6
Inversed-modeling: Case study
Inverse dispersion models:
Utilized models: EPA regulatory AERMOD and the Heavy Gas dispersion model for Steady-state (HEGADAS-S).
Notes: 6

## Slide 7
Inversed-modeling: Wind complexities
Fluid dynamic model suggests:
wind speeds at water level significantly differ from wind speed at 6 m above ground level
emission rate is not uniform at every point over pond’s surface. Emissions are mainly released from up-wind part of the pond.
Notes: 7

## Slide 8
Inversed-modeling: Results vary with techniques used
Chart: Canisters
| S0 | S1 | S2 | S3 | S4 | S5 | S6 | S7 | S8 | S9
C2 | 6.5257 | 21.5409 | 11.5757 | 11.132 | 33.5055 | 7.0242 | 4.5525 | 6.7965 | 22.7285 | 83.6361
C3 | 2.1844 | 14.717 | 8.651 | 6.3637 | 17.1284 | 0.73097 | 2.2243 | 2.8581 | 7.8737 | 33.5256
C4 | 6.566 | 20.945 | 27.777 | 47.799 | 16.932 | 11.076 | 5.68 | 12.927 | 14.413 | 39.73
C5 | 1.809 | 23.856 | 15.5805 | 21.6435 | 5.984 | 2.201 | 2.13 | 6.1855 | 9.017 | 14.8625
C6 | 0.402 | 66.74 | 48.8565 | 36.3075 | 15.572 | 1.42 | 1.917 | 7.8535 | 9.727 | 10.6575
C7 | 0.402 | 85.839 | 70.5 | 60.066 | 21.692 | 2.911 | 0.852 | 8.9655 | 5.68 | 7.3225
C8 | 0.871 | 36.281 | 24.0405 | 29.61 | 7.004 | 0.781 | 1.278 | 0.834 | 0.71 | 2.1025
C9 | 2.278 | 8.165 | 5.7105 | 4.1595 | 4.148 | 2.201 | 1.633 | 4.1005 | 2.982 | 2.32
C10+ | 2.01 | 5.183 | 4.089 | 3.807 | 1.564 | 1.136 | 2.13 | 0.834 | 0.994 | 1.885
Chart: Canister
| S0 | S1 | S2 | S3 | S4 | S5 | S6 | S7 | S8 | S9
C2 | 0 | 3.3239 | 5.4344 | 11.4372 | 13.0175 | 0.023116 | 0.00027469 | 6.9885e-05 | 0 | 1.3836
C3 | 0 | 2.3495 | 4.0808 | 8.3028 | 9.3802 | 0.01709 | 0.00022235 | 5.7677e-05 | 0 | 0.80285
C4 | 0 | 6.0518 | 10.4408 | 21.3049 | 24.1068 | 0.043956 | 0.00056071 | 0.00014536 | 0 | 2.0518
C5 | 0 | 3.2273 | 5.6036 | 11.3931 | 12.8587 | 0.023525 | 0.00030186 | 7.8276e-05 | 0 | 1.0566
C6 | 0 | 7.859 | 13.3294 | 27.4031 | 31.1149 | 0.056617 | 0.00069641 | 0.00018063 | 0 | 2.6563
C7 | 0 | 13.3493 | 21.7974 | 45.6321 | 52.2748 | 0.094671 | 0.0010797 | 0.00028037 | 0 | 4.5819
C8 | 0 | 5.1654 | 8.7572 | 18.0129 | 20.4249 | 0.037187 | 0.00045792 | 0.00011871 | 0 | 1.7476
C9 | 0 | 0.72661 | 1.2902 | 2.5967 | 2.8488 | 0.0054209 | 7.1364e-05 | 1.8458e-05 | 0 | 0.19384
C10+ | 0 | 0.43428 | 0.77126 | 1.5507 | 1.7443 | 0.003232 | 4.2199e-05 | 1.0925e-05 | 0 | 0.11695
Chart: Canister
| S0 | S1 | S2 | S3 | S4 | S5 | S6 | S7 | S8 | S9
C2 | 0 | 6.9257 | 11.7195 | 17.067 | 9.4168 | 0.044122 | 0.00059269 | 0.00015077 | 0 | 2.2629
C3 | 0 | 4.865 | 8.7913 | 12.0341 | 6.1648 | 0.032389 | 0.00047902 | 0.00012431 | 0 | 1.2832
C4 | 0 | 12.5346 | 22.4242 | 30.9947 | 15.8994 | 0.083253 | 0.0012043 | 0.00031219 | 0 | 3.2733
C5 | 0 | 6.6827 | 12.035 | 16.526 | 8.4173 | 0.044527 | 0.00064833 | 0.00016812 | 0 | 1.6844
C6 | 0 | 17.8565 | 31.4371 | 44.0753 | 22.7065 | 0.11797 | 0.0016468 | 0.0004269 | 0 | 4.6629
C7 | 0 | 27.704 | 46.8158 | 68.1612 | 35.4355 | 0.18105 | 0.0023194 | 0.00060216 | 0 | 7.3307
C8 | 0 | 10.7058 | 18.8093 | 26.4298 | 13.5693 | 0.070636 | 0.00098459 | 0.00025495 | 0 | 2.7868
C9 | 0 | 1.5025 | 2.7713 | 3.7155 | 1.7545 | 0.010232 | 0.00015354 | 3.9644e-05 | 0 | 0.29663
C10+ | 0 | 0.89832 | 1.6567 | 2.2293 | 1.1162 | 0.0061053 | 9.083e-05 | 2.3464e-05 | 0 | 0.17844
Chart: Canister
| S0 | S1 | S2 | S3 | S4 | S5 | S6 | S7 | S8 | S9
C2 | 0 | 5.2678 | 10.0728 | 13.6737 | 9.7315 | 2.2916 | 3.0017 | 4.0257 | 0.6731 | 1.4309
C3 | 0 | 3.9526 | 7.558 | 10.2598 | 7.3019 | 1.7195 | 2.2522 | 3.0206 | 0.50505 | 1.0737
C4 | 0 | 11.3693 | 21.7397 | 29.5112 | 21.0031 | 4.9458 | 6.4783 | 8.6884 | 1.4527 | 3.0883
C5 | 0 | 6.8323 | 13.0642 | 17.7345 | 12.6216 | 2.9722 | 3.8931 | 5.2212 | 0.873 | 1.8559
C6 | 0 | 17.8226 | 34.0793 | 46.2621 | 32.9246 | 7.7531 | 10.1555 | 13.62 | 2.2773 | 4.8412
C7 | 0 | 26.1734 | 50.0471 | 67.9381 | 48.3514 | 11.3859 | 14.9138 | 20.0016 | 3.3443 | 7.1095
C8 | 0 | 10.4125 | 19.9101 | 27.0277 | 19.2355 | 4.5296 | 5.9331 | 7.9572 | 1.3305 | 2.8284
C9 | 0 | 1.4267 | 2.7281 | 3.7034 | 2.6357 | 0.62065 | 0.81296 | 1.0903 | 0.1823 | 0.38755
C10+ | 0 | 0.78085 | 1.4931 | 2.0269 | 1.4425 | 0.33968 | 0.44494 | 0.59672 | 0.099774 | 0.2121
Comparisons of NMHC concentration distributions (excluding alcohols)
Canister measurements
HEGADAS-S full-pond
HEGADAS-S partial-pond
AERMOD open-pit
Notes: 8

## Slide 9
Inversed-modeling consistently overestimate flux-chamber measurements
Measurement Campaign | Means of estimation | Alkanes | Alkenes | Aromatics | Alcohols | Total NMHC
April 2015 (Landfarm) | FLUX | 287.5 | 4.6 | 83.8 | 2.4 | 378.3
 | FLUX-C | The developed wind correction factors are not applicable for air-soil exchange interface |  |  |  | 
 | AERM | 2891.0 | 0.4 | 1068.8 | 29.6 | 3990
 | HEGA | 2690.4 | 0.8 | 1027.1 | 11.1 | 3729
Apr2016 (Pond) | FLUX | 34.0 | 0.0 | 60.4 | 201.5 | 296
 | FLUX-C | 37.9 | 0.0 | 67.1 | 659.6 | 765
 | AERM-1 | 714.8 | 1.3 | 628.1 | 312.8 | 1657
 | HEGA-1 | Was not performed due to calm and strongly variate wind |  |  |  | 
 | AERM-2 | 525.1 | 16.0 | 490.6 | 2658.2 | 3690
 | HEGA-2 | 149.6 | 6.2 | 142.9 | 866.3 | 1165
 | AERM-3 | 659.7 | 26.8 | 748.6 | 1729.3 | 3164
 | HEGA-3 | 495.1 | 15.1 | 388.4 | 1148.4 | 2047
Jul2016 (Pond) | FLUX | 24.4 | 0.0 | 67.6 | 108.8 | 201
 | FLUX-C | 46.0 | 0.1 | 123.3 | 545.6 | 715
 | AERM-1 | 261.7 | 4.2 | 265.8 | 1327.0 | 1859
 | HEGA-1 | 114.9 | 1.5 | 143.3 | 686.3 | 946
 | AERM-2 | 417.4 | 3.9 | 1063.7 | 1935.8 | 3421
 | HEGA-2 | 160.8 | 0.8 | 424.0 | 728.8 | 1314
Geometric means of ratios | HEGA/FLUX-C | 5.3 | 2.7 | 3.6 | 1.8 | 2.5
 | AERM/FLUX-C | 11.5 | 5.2 | 7.5 | 2.8 | 4.2
 | HEGA/AERM | 0.5 | 0.5 | 0.5 | 0.4 | 0.5
Notes: 9

## Slide 10
Mass-Transfer Law
F = S c
Flux
(g/m2/h)
Mass-transfer coefficient
(m/h)
Pond concentration
(g/m3)
Proportionality between flux and concentration.
S may depend on:
temperature, wind speed, salinity,
nature of compound
Notes: 10

## Slide 11
WATER-9
Semi-empirical algorithm for estimating S (H = Henry’s law coefficient, it
anti-correlates with solubility.)
Blue, tan, black:
Temperature modulation.
Salinity modulation is
about 30% to 50% in H.
Notes: 11

## Slide 12
WATER-9 prediction of flux chamber results.
Accurate to within about 1 order of
magnitude over a range of about
5 orders.
Notes: 12

## Slide 13
Wind Speed Correction
Based on WATER-9
Notes: 13

## Slide 14
Basin-wide scale up
Notes: 14

## Slide 15
Acknowledgements
Funding Provided By
  U.S. Department of Energy/Research Partnership to Secure Energy for America (Contract No. 12122-15)
  Bureau of Land Management (Cooperative Agreement No. L13AC00292)
  Uintah Impact Mitigation Special Service District
  GSI, Inc./State of Wyoming
  Utah State and Institutional Trust Lands Administration
Notes: 15

## Slide 16
Thank You
binghamresearch.usu.edu