SMITHFIELD CITY

STORM WATER

MANAGEMENT PROGRAM

April 2003

By: J-U-B ENGINEERS, Inc.

INTRODUCTION

Polluted storm water runoff is often transported to municipal separate storm sewer systems (MS4s) and ultimately discharged into local rivers and streams without treatment.  EPA’s Storm Water Phase II Rule establishes an MS4 storm water management program that is intended to improve the Nation’s waterways by reducing the quantity of pollutants that are introduced into storm sewer systems during storm events.  Common pollutants include oil and grease from roadways, pesticides and fertilizers from lawns, sediment from construction sites, and carelessly discarded trash, such as cigarette butts, paper wrappers, and plastic bottles.  When deposited into nearby waterways through MS4 discharges, these pollutants can impair the waterways, thereby discouraging use of the resource, contaminating drinking water supplies, and interfering with the habitat for fish, other aquatic organisms, and wildlife.

In 1990, EPA promulgated rules establishing Phase I of the National Pollutant Discharge Elimination System (NPDES) storm water program.   The Phase I program for MS4s requires operators of “medium” and “large” MS4s, that is, those that generally serve populations of 100,000 or greater, to implement a storm water management program as a means to control polluted discharges from these MS4s.  The Storm Water Phase II Rule extends coverage of the NPDES storm water program to certain “small” MS4s but takes a slightly different approach to how the storm water management program is developed and implemented.

Storm Water Management Program

A Storm Water Management Program should:

1	Reduce the discharge of pollutants to the “maximum extent practicable” (MEP);

2	Protect water quality;

3	Satisfy the appropriate water quality requirements of the Clean Water Act; and

4	Be phased in over a five year period.

Storm water management programs must include:

1	Best Management Practices (BMPs) for each of the six minimum control measures;

1.	Public Education and Outreach

2.	Public Participation/Involvement

3.	Illicit Discharge Detection and Elimination

4.	Construction Site Runoff Control

5.	Post-Construction Runoff Control

6.	Pollution Prevention/Good Housekeeping

1	Measurable goals for each minimum control measure (i.e., narrative or numeric standards used to gauge program effectiveness);

2	Estimated months and years in which actions to implement each measure will be undertaken, including interim milestones and frequency; and

3	The person or persons responsible for implementing or coordinating the storm water program.

Permit Application and Notice of Intent

Phase II Rule encourages the development of a storm water management program by requiring a Notice of Intent (NOI) describing the storm water management program to be submitted to the NPDES permitting authority.  The Notice of Intent becomes the permit application.

Cities required to permit under Phase II are allowed to cooperate and work together with neighboring cities in the application process.  The permittee may join with a Phase I city or another Phase II city in applying for a permit.  The individual MS4s may share responsibility for program development with neighboring communities and/or take advantage of existing local or state programs.

Permit Requirements

The chosen measurable goals, submitted in the Notice of Intent as a permit application, become the required storm water management program; however, the NPDES permitting authority can require changes in the mix of chosen BMPs and measurable goals if all or some of them are found to be inconsistent with the provisions of the Phase II Final Rule.  Likewise, the permittee can change its mix of BMPs if it determines that the program is not effective as it could be.

Reports

Reports must be submitted annually during the first permit term.  (Up to 5 yrs)  For subsequent permit terms, reports must be submitted in years 2 and 4 only, unless the NPDES permitting authority requests more frequent reports.  The reports must include:

1	The status of compliance with permit conditions, including an assessment of the appropriateness of the selected BMPs and progress toward achieving the selected measurable goals for each minimum measure;

2	Results of any information collected and analyzed, including monitoring data if any;

3	A summary of the storm water activities planned for the next reporting cycle;

4	A change in any identified BMP or measurable goals for any minimum measure; and

5	Notice of relying on another governmental entity to satisfy some of the permit obligations (if applicable).

Record Keeping

Records required by the NPDES permitting authority must be kept for at least 3 years and made accessible to the public at reasonable times during regular business hours.  Records need not be submitted to the NPDES permitting authority unless the permitee is requested to do so.

Deadlines

The NPDES permitting authority issues general permits for regulated small MS4s by December 9, 2002.

Operators of “automatically designated” regulated small MS4s in urbanized areas submit their permit applications within 90 days of permit issuance, no later than March 10, 2003.

Operators of regulated small MS4s designated by the permitting authority submit their permit applications within 180 days of notice

Regulated small MS4 storm water management programs fully developed and implemented by the end of the first permit term, typically a 5-year period

Penalties

The NPDES permit that the operator of a regulated small MS4 is required to obtain is federally enforceable, thus subjecting the permitee to potential enforcement actions and penalties by the NPDES permitting authority if the permittee does not fully comply with application or permit requirements.  This federal enforceability also includes the right for interested parties to sue under citizen suit provision (section 405) of CWA.

Notice of Intent

The Notice of Intent has been prepared in conjunction with this document and a copy has been included in the Appendix.

Chapter 2 contains a description of the community-specific Storm Water Management Program for Smithfield City.  The Program includes the following;

2	Best Management Practices (BMPs) for each of the six minimum control measures;

1.	Public Education and Outreach

2.	Public Participation/Involvement

3.	Illicit Discharge Detection and Elimination

4.	Construction Site Runoff Control

5.	Post-Construction Runoff Control

6.	Pollution Prevention/Good Housekeeping

4	Measurable goals for each minimum control measure (i.e., narrative or numeric standards used to gauge program effectiveness);

5	Estimated months and years in which actions to implement each measure will be undertaken, including interim milestones and frequency; and

6	The person or persons responsible for implementing or coordinating the storm water program.

SMITHFIELD CITY CHARACTERISTICS

General Information

The Smithfield City Storm Drain System falls under the Public Works Department for the City.  The Public Works Director can be contacted at the following address and phone number:

Mr. Doug Petersen

58 South 800 West

Smithfield, UT 84335

(435) 563-6226

| Population: | 7,261 |
| --- | --- |
| Size: | 4.25 sq. miles |
| Geographic Description: | 7 miles North of Logan. Located on the East side of Cache Valley with elevations varying between 4520 ft. to 4870 ft. |
| Receiving Waters: | Smithfield is a drainage basin for the Bear River. |
| Annual Precipitation: | 17.36 inches per year |
| Type of Community: | A small rural city with high rates of residential growth that are expected to continue for many years. |
| Latitude: | 41.83° N |
| Longitude: | 111.82° W |

Storm Drain System

The Smithfield storm water system consists of curb and gutters, culverts, a few typical piped sections, swales and canals.  Most storm water facilities continue to drain into irrigation canals where they empty into Summit Creek, a natural waterway that empties into the Bear River or continue northward and eventually empty into the Bear River.  The canals have served as the recipient for storm water flows since the city’s establishment.  Very few controls exist within the system.  Many of the streets use curb and gutter to collect storm water runoff with the remaining using swales or ditches.

Storm Water Management Agreement

The Utah Association of Conservation Districts as part of the Bridging the Headgate Partnership is working to facilitate a Storm Water Management Agreement between Irrigation Companies and Municipalities.  They are currently in the process of establishing a legal document to serve as a template whereby the irrigation companies may allow the municipalities to use their canals for storm water runoff.  This document will define a relationship that allows the Irrigation Companies to maintain and regulate the canal while receiving revenue from the municipalities to offset costs of maintaining and operating the canals.  The relationship allows for flexibility in the management of and responsibilities that pertain to the canals.  The agreement will address responsibility for cases of flooding and accidents.  It will also address additional storm water to be added to the system and the party that will give approval.  This document will be helpful to many communities in establishing a Storm Water Management Agreement with the Irrigation Companies.

Sewer System

The city is served by a sanitary sewer system that is treated in Logan City.  The city has an ordinance requiring any new development within 300 feet of the existing sanitary sewer to connect.  There are some existing septic tank systems in the city and some new developments with septic tanks, but the trend is toward connecting to the sanitary sewer system as the network is enlarged.

History

Smithfield, located in Cache County, is eight miles north of Logan. Smithfield was settled in October of 1859 by Seth Langton and by Robert and John Thornley. The first settlement was located approximately one-half mile west of the present site and was originally called Summit, because of its location on Summit Creek. The site was later renamed Smithfield after John Glover Smith in 1860.

The dairy industry is important to Smithfield, and in 1892 the Smithfield Dairy Company built its plant--which was later taken over by Sego Milk Products. In 1920 the Morgan Pea Factory began business and was later bought by Del Monte Foods; it has since been turned into a can-making factory. Some current businesses in Smithfield are Cantwell Brothers Lumber, Smithfield Livestock Auction, and Smithfield Implement.

Since the 1970’s, Smithfield has grown rapidly in population. Today, the city is a thriving mix of residential, commercial, industrial and agricultural prosperity.

Local Water Quality Concerns

The water quality within the city of Smithfield is relatively good.  None of the streams or waterways have been identified as protected under Section 303(d) of the Clean Water Act.  The hope and intent of this Storm Water Management program (SWMP) is to maintain that status and possibly even improve the current water quality.

The storm water in Smithfield City drains to a series of canals and ditches where it is transported to Summit Creek or the Bear River.  At present, the city has not encountered any major problems related to the canals capacities, however there has been a large amount of development and the last four years have been relatively dry.

Like most communities in the valley, the biggest concerns involve:

1	sediment loads coming from disturbed sites and streets,

2	fertilizers and pesticides coming from lawns and farmlands,

3	oils and grease coming from the roadways,

4	animal waste coming from dairies with runoff and when flushed out.

Hyde Park’s SWMP has been geared toward small city applications, targeting the pollutants mentioned.  The focus of this plan is to do what we can within the community, trying to stay in harmony with the rural nature of the community and within the existing budget structure.

Steering Committee

A steering committee was formed in the spring of 2002 for the purpose of addressing the above mentioned water quality items and consider options to develop a storm water management program.  The steering committee includes members from the community including:

| Name | Representing |
| --- | --- |
| Ray Winn | Mayor |
| Jeff Gittins | Councilman |
| Clay Bodily | Public Works |

PUBLIC EDUCATION AND OUTREACH

Phase II Requirements

1.	The operator of a regulated small MS4 needs to implement a public education program to distribute educational materials to the community, or conduct equivalent outreach activities about the impacts of storm water discharges on local water bodies and the steps that can be taken to reduce storm water pollution; and

2.	Determine the appropriate best management practices (BMPs) and measurable goals for this minimum control measure.

Summary of Existing Efforts

Educational Materials

All cities in Cache County contract with Service Area #1 to provide garbage collection, waste services, and a recycling program.  The Cache County Council serves as board for Service Area #1, which in turn contracts with Logan City Environmental Division to provide the services.  There are educational materials covering subjects of recycling, waste reduction, and proper disposal that are available at the local landfill.  (See Appendix D)

Recycling Facilitator

In contracting with Service Area #1 to provide waste services, a recycling program is included.  There is a Recycling Facilitator who currently works with the local schools to teach about recycling and natural resources.  In the 2001-2002 school year the Recycling Educator was able to teach 5th grade classes in all of the Logan City and Cache County school districts about recycling and litter prevention.

City used Media

Smithfield City was a website that is located at:

http://www.smithfieldcity.org

There is a newsletter that is sent out five times a year.  It informs the public of current issues and upcoming events.

Plan and Implementation Measures

In order to help meet the goals and objectives of this SWMP, Smithfield City has chosen to adopt the following BMPs.  Each BMP is cross referenced alphabetically by code in Appendix A to a fact sheet that describes the BMP, its applicability, its limitations, and its effectiveness.  Only those BMPs listed below will be utilized by Smithfield City as part of their SWMP at the present time.

| BMP | Code |
| --- | --- |
| Educational Materials | EM |
| Classroom Education on Storm Water | CESW |
| Public Education / Participation | PEP |
| Using Media | UM |
| Materials Use | MU |
| Housekeeping Practice | HP |

In order to more fully realize the benefit of the BMP the city has set the following goals.  The goals set along with the existing efforts fulfill the requirements of the Final Storm Water Phase II Rule for Education and Outreach.

| Public Education And Outreach |
| --- |
| MANAGEMENT PLAN | MEASURABLE GOAL | COST | CONTACT PERSON |
| Establish and participate in an Inter-Local Storm Water Education / Public Participation Program to teach the public about storm water and the effects that citizens can have on it. | 1 yr 2-5 yr | Establish agreement with county or surrounding communities to establish an Inter-Local Storm Water Education / Public Participation Program. Implement program | $200 To be determined | Clay Bodily |
| Inform the public about new ordinances and the effects of noncompliance. Educate the public on the importance of protecting storm water from improperly used, stored, and disposed of pollutants by using newsletters and the City website | 1 yr 1-5 yr | Send flyer twice a year with newsletter Post information on the City website and update twice a year | $525/year | Dean Clegg |

PUBLIC PARTICIPATION / INVOLVEMENT

Phase II Requirements

1.	Comply with applicable State, Tribal, and local public notice requirements; and

2.	Determine the appropriate best management practices (BMPs) and measurable goals for this minimum control measure.

Summary of Existing Efforts

Steering Committee

A “Storm Water Steering Committee” consisting of city officials and staff members was formed in June of 2002 and has taken an active role in selecting the BMPs and developing the initial SWMP for the city.

Recycling Program

All cities in Cache County contract with Service Area #1 for waste management services which include a recycling program.  Logan City Environmental Division is contracted by Service Area #1 to provide services to the cities.

The program reduces solid waste by recycling and offers proper disposal options for hazardous wastes that can be difficult to dispose of, thereby preventing storm water contamination due to improper disposal of hazardous wastes and solids.  The landfill accepts: cardboard, newspaper, aluminum cans, tin/steel cans, plastic pop bottles, plastic milk jugs, green waste, aluminum scrap, ferrous metals, tires, used oil, oil filters, antifreeze, carpet pad, batteries, wood pallets, mixed paper on site for recycling.

Drop-sites have been set up through out the county to facilitate recycling.  The drop sites accept cardboard, newspaper, mixed paper, aluminum cans, tin/steel cans, plastic pop bottles, plastic milk jugs, glass, and green waste.

The current drop-site for the city is located north of the fire station.

Green Waste Collection

A curbside green waste collection program exists from Smithfield to Providence.  It is administered by the Logan environmental Division acting under contract for Service Area #1 who contracts with the individual cities of Cache County to provide waste services.  The program currently has about 1,000 members who participate in a curbside pick up program for green waste recycling for a monthly fee.  The Logan Landfill has a green waste facility where green waste can be dropped off and it is either composted or made into wood chips or firewood.  The green waste facility encourages donations by offering $10 of compost or wood chip material for ten loads of compost materials dropped off.  This program encourages reuse of an otherwise useless material that could become a solid contaminant in storm water.

Other Community Groups

There are two other community groups that are actively engaged in protecting the local environment.  They are “Friends of Smithfield Canyon” and “Birch Creek Golf Course Volunteer Cleanup Committee”.

Birch Creek Golf Course Cleanup

Every spring, a community volunteer group of golfers pick up trash around the golf course.

Plan and Implementation Measures

In order to help meet the goals and objectives of this SWMP, Smithfield City has chosen to adopt the following BMPs for use within our city as applicable.   Each BMP is cross referenced alphabetically by code to a fact sheet that describes the BMP, its applicability, its limitations, and its effectiveness in Appendix A.

| BMP | Code |
| --- | --- |
| Service Group Participation | SGP |
| Community Cleanup | CC |
| Storm Channel / Creek Maintenance | SCCM |
| Stream Cleanup and Monitoring | SCM |
| Form a Watershed Organization | WO |

In order to more fully realize the benefit of the BMP, the city has set the following

goals.  The goals set along with the existing efforts fulfill the requirements of the Final Storm Water Phase II Rule for Public Involvement and Participation.

| Public Participation / Involvement |
| --- |
| MANAGEMENT PLAN | MEASURABLE GOAL | COST | CONTACT PERSON |
| Encourage citizens and scout troops to clean stream banks and roadsides | 1-5 yr | Prepare list of potential projects and distribute | $150/year | Clay Bodily |
| Maintain steering committee and continue with meetings to assess progress and continue making plans. | 1-5 yr | Conduct 2 meetings a year | $150/year | Clay Bodily or Jeff Gittins |
| Establish and Participate in Inter-Local Storm Water Education / Public Participation Program | 1-5 yr | See Education Measurable Goals |  |  |

ILLICIT DISCHARGE DETECTION AND ELIMINATION

Phase II Requirements

1.	Must include a storm sewer system map, showing the location of all outfalls and the names and location of all waters of the United States that receive discharges from those outfalls;

2.	Through an ordinance, or other regulatory mechanism, a prohibition (to the extent allowable under State, Tribal, or local law) on non-storm water discharges into the MS4, and appropriate enforcement procedures and actions;

3.	A plan to detect and address non-storm water discharges, including illegal dumping, into the MS4;

4.	The education of public employees, businesses, and the general public about the hazards associated with illegal discharges and improper disposal of waste; and

5.	The determination of appropriate best management practices (BMPs) and measurable goals for this minimum control measure.

Summary of Existing Efforts

Illicit Discharge

Smithfield City does not currently have an ordinance designed to specifically prohibit illicit discharges to the storm sewer system.

Hazardous Spills

Currently, reports of spills are handled by the Fire Department, Logan Service Center or County Health Department.

The City has not generally experienced problems with individuals or businesses illicitly connecting their sanitary waste water piping to storm drains.  More-common types of illicit discharges include spills from highway accidents, concrete truck wash out water, and general household waste.

Storm Water System Map

See Appendix B.

Plan and Implementation Measures

In order to help meet the goals and objectives of this SWMP, Smithfield City has chosen to adopt the following BMPs for use within our city as applicable.   Each BMP is cross referenced alphabetically by code to a fact sheet that describes the BMP, its applicability, its limitations, and its effectiveness in Appendix A.

| BMP | Code |
| --- | --- |
| Ordinance Development | OD |
| Illegal Dumping Controls | IDC |
| Identify Illicit Connection | IIC |
| Non-Storm Water Discharge to Drains | NSWD |

In order to more fully realize the benefit of the BMP the city has set the following goals. The goals set along with the existing efforts fulfill the requirements of the Final Storm Water Phase II Rule for Illicit Discharge Detection and Elimination.

| Illicit Discharge Detection And Elimination |
| --- |
| MANAGEMENT PLAN | MEASURABLE GOAL | COST | CONTACT PERSON |
| Adopt model ordinance prohibiting discharge of non-storm water into the system and dumping into the storm system including grass clippings on stream and canal banks. and prescribing a punishment for violation | 1 yr 2 yr | Review model ordinance with steering committee Pass through city council | $1150 | Clay Bodily |
| Involve public and city employees in a watch and report program Post signs at critical locations indicating that persons dumping illegally will be prosecuted | 1-5 yr 2-5 yr 2 yr | Set up a procedure for handling citizen reports and inform public through newsletter Provide the public with forms to use 2 signs posted | $250 $250 $200 | Clay Bodily or Doug Peterson |
| Facilitate alternate disposal options for green waste to reduce illegal dumping | 2-5 yr | Place two green bins on the east and West sides of the community (notify residents when bins are available) | No additional cost | Clay Bodilyplaced 3-22-2004 |
| Placed Dry water monitoring to detect illicit connections | 2-5 yr | Send a crew out in the summer months to monitor flows in storm drains during ‘dry’ events | $900/year | Clay Bodily |
| Education of public employees, businesses, and the general public about the hazards associated with illegal discharges and improper disposal of waste through newsletter discussed in Public Education and through the annual meeting with city commerce. | 1-5 yr | Discuss illegal discharges in monthly newsletter | $250/year | Doug Peterson |
| Map storm water inlets and outfalls | 1 yr. | Have an electronic copy that can be updated | $200/year | Clay Bodilyupdated 4-2-2004 |
| Develop a procedure to gain approval from the irrigation companies for storm water discharge. | 1 yr 2-5 yr | Develop a cooperative agreement with required approvals on final plat Begin implementation | $5,000 | Clay Bodily Storm drain along 200w |

CONSTRUCTION SITE RUNOFF CONTROL

Phase II Requirements

1.	Have an ordinance or other regulatory mechanism requiring the implementation of proper erosion and sediment controls, and controls for other wastes, on applicable construction sites;

2.	Have procedures for site plan review of construction plans that consider potential water quality impacts;

3.	Have procedures for site inspection and enforcement of control measures;

4.	Have sanctions to ensure compliance (established in the ordinance or other regulatory mechanism);

5.	Establish procedures for the receipt and consideration of information submitted by the public; and

6.	Determine the appropriate best management practices (BMPs) and measurable goals for this minimum control measure.

Summary of Existing Efforts

Ordinances

There are currently no City ordinances or specifications related to erosion and sediment control.

Site Plan Review

There are currently no procedures for site plan review of construction plans that consider potential water quality impacts such as requiring submittal of an erosion control plan as part of the building permit process.

Site Inspector

There is currently one public works inspector who oversees local construction.  He is concerned with sewer connections, storm drain and streets.  Although no city ordinances currently exist regarding erosion control, the inspectors make decisions using good judgment of what proper construction technique is and can require contractors to clean up streets and causes of contamination.

Standard Drawings and Specifications

The city is considering reviewing and refining their set of standard drawings and specifications.

Plan and Implementation Measures

In order to help meet the goals and objectives of this SWMP, Smithfield City has chosen to adopt the following BMPs for use within our city as applicable.   Each BMP is cross referenced alphabetically by code to a fact sheet that describes the BMP, its applicability, its limitations, and its effectiveness in Appendix A.

| BMP | Code |
| --- | --- |
| Erosion Control Plan | ECP |
| Landscape & Irrigation Plan | LIP |
| Establish/Compile Design Standards | ECDS |
| Certification and Inspector Training | CCIT |
| Building, Repair, Remodeling, & Construction | BRRC |
| Dust Controls | DC |
| Temporary and Permanent Seeding | TPS |
| Silt Fence | SF |
| Straw Bales | SB |
| Contaminated or Erodible Surface Areas | CESA |
| Temporary Drains and Swales | TDS |

In order to more fully realize the benefit of the BMP the city has set the following goals.  The goals set along with the existing efforts fulfill the requirements of the Final Storm Water Phase II Rule for Construction Site Runoff Control.

| Construction Site Runoff Control |
| --- |
| MANAGEMENT PLAN | MEASURABLE GOAL | COST | CONTACT PERSON |
| Adopt an ordinance requiring proper erosion and sediment controls, and controls for other wastes with a regulatory mechanism (including above ground fuel storage tanks with isolation areas). Address mud tracked onto streets by machinery, and dust control. | 1 yr 2 yr | Review in Steering Committee Approve by city council | $3200/year $250 | Clay Bodily |
| Require Erosion Control and Re-vegetation Plans prior to new developments one acre in size or larger. Inform what the requirements and options are. | 1 yr 1 yr | Establish a guideline or example of a control plan Establish minimum requirements that address appropriate issues | $650/year $650/year | Clay Bodily |
| Include the following erosion protection measures in the information handed out when seeking a building permit: silt fence, straw bales, earth berm for runoff diversion and road watering to minimize dust during road construction | 1-5 yr | Update information | $250/year | Clay Bodily |
| Monitor compliance with building inspector and establish procedures for inspections and train employees (Consider using an Inter-Local Training Meeting.) | 1 yr 1-5 yr 1-5 yr | Establish procedures (written form) Have one employee training meeting Inspect construction sites larger than one acre on a monthly basis. File a report on the findings. Take steps to ensure corrective action. Monitor all construction sites for mud, dust, etc. | $300/year $250/year $2400 | Clay Bodily |

POST CONSTRUCTION RUNOFF CONTROL

Phase II Requirements

1.	Develop and implement strategies which include a combination of structural and/or non-structural best management practices (BMPs);

2.	Have an ordinance or other regulatory mechanism requiring the implementation of post construction runoff controls to the extent allowable under State, Tribal, or local law,

3.	Ensure adequate long-term operation and maintenance of controls;

4.	Determine the appropriate best management practices (BMPs) and measurable goals for this minimum control measure.

Summary of Existing Efforts

Ordinances

There are not currently any ordinances development codes or guidelines to address storm water runoff from construction and new development sites.

Landscaping Plan Review

Developers are required to present a plan outlining landscaping plans to the city.

Plan and Implementation Measures

In order to help meet the goals and objectives of this SWMP Smithfield City has chosen to adopt the following BMPs for use within our city as applicable.   Each BMP is cross referenced alphabetically by code to a fact sheet that describes the BMP, its applicability, its limitations, and its effectiveness in Appendix A.

| BMP | Code |
| --- | --- |
| Ordinance Development | OD |
| Land Use Planning / Management | LUPM |
| Zoning | ZO |
| Grassed Swales | GS |
| Seeding and Planting | SP |
| Alternate Turnarounds | AT |

In order to more fully realize the benefit of the BMP, the city has set the following

goals. The goals set along with the existing efforts fulfill the requirements of the Final Storm Water Phase II Rule for Post Construction Runoff Control.

| Post Construction Runoff Control |
| --- |
| MANAGEMENT PLAN | MEASURABLE GOAL | COST | CONTACT PERSON |
| Adopt ordinance setting minimum requirements for landscaping and requiring landscaping on all residential and commercial developments. Set requirements for open spaces, detention ponds, and alternate cul-de-sac turnarounds | 1 yr 2 yr | Review in steering committee Review and pass by city council | $350 $500 | Planning & Zoning Committee |
| Have a storm water drainage system for 1000 E from 50 S to 200 N that drains into a detention pond on Birch Creek Golf Course | 2 yr | Completed system | $40,000 | Clay Bodily Or Jim Gass |
| Develop a procedure to gain approval from the irrigation companies for storm water discharge | 1-5 yr | See Measurable Goal in Illicit Discharge Detection and Elimination Section |  |  |

POLLUTION PREVENTION / GOOD HOUSEKEEPING

Phase II Requirements

1.	Develop and implement an operation and maintenance program with the ultimate goal of preventing or reducing pollutant runoff from municipal operations into the storm sewer system;

2.	Include employee training on how to incorporate pollution prevention / good housekeeping techniques into municipal operations such as park and open space maintenance, fleet and building maintenance, new construction and land disturbances, and storm water system maintenance.  (Training materials available from EPA).

3.	Determine the appropriate best management practices (BMPs) and measurable goals for this minimum control measure.

Summary of Existing Efforts

The city currently maintains the following items in its storm water system.

| Item | Maintenance |
| --- | --- |
| Catch Basins | Clean as needed |
| Detention Basins | No procedures |
| Ditches and Canals | Cooperate with Canal co. |
| Street Sweeping | Cleaning in the spring |

Recycling Program

The City participates in a recycling program.  (See Recycling Program on pg. 9)

Educational Materials

The City has educational materials. (See Educational Material on pg. 8)

Green Waste Collection

The City has a Green Waste Collection program (See Green Waste Collection on pg. 11)

Operations

Salt is stored under cover to prevent contamination of storm water and other areas.

Plan and Implementation Measures

In order to help meet the goals and objectives of this SWMP Smithfield City has chosen to adopt the following BMPs for use within our city as applicable.   Each BMP is cross referenced alphabetically by code to a fact sheet that describes the BMP, its applicability, its limitations, and its effectiveness in Appendix A.

| BMP | Code |
| --- | --- |
| BMP Inspection and Maintenance | BMPIM |
| Long Term Operation and Maintenance | LTOM |
| Street Cleaning | SC |
| Catch Basin Cleaning | CBC |
| Employee Training | ET |
| Building and Grounds Maintenance | BGM |
| Area Control Procedures | ACP |
| Inspection and Maintenance | IM |

In order to more fully realize the benefit of the BMP, the city has set the following

goals.  The goals set along with the existing efforts fulfill the requirements of the Final Storm Water Phase II Rule for Pollution Prevention/Good Housekeeping.

| Pollution Prevention / Good Housekeeping |
| --- |
| MANAGEMENT PLAN | MEASURABLE GOAL | COST | CONTACT PERSON |
| Establish schedule for maintenance activities including parking lot cleaning, street sweeping, catch basins, curb and gutter cleaning. | 1-5 yr | Have a written policy and schedule to refer to | $2,500 | Clay Bodily or Lyle Izat Done Sept 2003by Matt |
| Offer in-house training to city employees to promote a clear understanding of the impacts of various activities to storm water and promote employee ownership of the problems and the solutions. (Consider using an Inter-Local Training Meeting) | 1 yr 2-5 yr | Obtain information Instigate employee training meeting | $600 | Doug Petersen |

MEASURABLE GOALS SUMMARY

| Public Education And Outreach |
| --- |
| MANAGEMENT PLAN | MEASURABLE GOAL | COST | CONTACT PERSON |
| Establish and participate in an Inter-Local Storm Water Education / Public Participation Program to teach the public about storm water and the effects that citizens can have on it. | 1 yr 2-5 yr | Establish agreement with county or surrounding communities to establish an Inter-Local Storm Water Education / Public Participation Program. Implement program | $200 To be determined | Clay Bodily |
| Inform the public about new ordinances and the effects of noncompliance. Educate the public on the importance of protecting storm water from improperly used, stored, and disposed of pollutants by using newsletters and the City website | 1 yr 1-5 yr | Send flyer twice a year with newsletter Post information on the City website and update twice a year | $525/year | Dean Clegg Febuary 2004 newsletter page 9 |

| Public Participation / Involvement |
| --- |
| MANAGEMENT PLAN | MEASURABLE GOAL | COST | CONTACT PERSON |
| Encourage citizens and scout troops to clean stream banks and roadsides | 1-5 yr | Prepare list of potential projects and distribute | $150/year | Clay Bodily |
| Maintain steering committee and continue with meetings to assess progress and continue making plans. | 1-5 yr | Conduct 2 meetings a year | $150/year | Clay Bodily or Jeff Gittins |
| Establish and Participate in Inter-Local Storm Water Education / Public Participation Program | 1-5 yr | See Education Measurable Goals |  |  |

| Illicit Discharge Detection And Elimination |
| --- |
| MANAGEMENT PLAN | MEASURABLE GOAL | COST | CONTACT PERSON |
| Adopt model ordinance prohibiting discharge of non-storm water into the system and dumping into the storm system including grass clippings on stream and canal banks. and prescribing a punishment for violation | 1 yr 2 yr | Review model ordinance with steering committee Pass through city council | $1150 | Clay Bodily |
| Involve public and city employees in a watch and report program Post signs at critical locations indicating that persons dumping illegally will be prosecuted | 1-5 yr 2-5 yr 2 yr | Set up a procedure for handling citizen reports and inform public through newsletter Provide the public with forms to use 2 signs posted | $250 $250 $200 | Clay Bodily or Doug Peterson |
| Facilitate alternate disposal options for green waste to reduce illegal dumping | 2-5 yr | Place two green bins on the east and West sides of the community (notify residents when bins are available) | No additional cost | Clay Bodily |
| Dry water monitoring to detect illicit connections | 2-5 yr | Send a crew out in the summer months to monitor flows in storm drains during ‘dry’ events | $900/year | Clay Bodily |
| Education of public employees, businesses, and the general public about the hazards associated with illegal discharges and improper disposal of waste through newsletter discussed in Public Education and through the annual meeting with city commerce. | 1-5 yr | Discuss illegal discharges in monthly newsletter | $250/year | Doug Peterson |
| Map storm water inlets and outfalls | 1 yr. | Have an electronic copy that can be updated | $200/year | Clay Bodily |
| Develop a procedure to gain approval from the irrigation companies for storm water discharge. | 1 yr 2-5 yr | Develop a cooperative agreement with required approvals on final plat Begin implementation | $5,000 | Clay Bodily |

| Construction Site Runoff Control |
| --- |
| MANAGEMENT PLAN | MEASURABLE GOAL | COST | CONTACT PERSON |
| Adopt an ordinance requiring proper erosion and sediment controls, and controls for other wastes with a regulatory mechanism (including above ground fuel storage tanks with isolation areas). Address mud tracked onto streets by machinery, and dust control. | 1 yr 2 yr | Review in Steering Committee Approve by city council | $3200/year $250 | Clay Bodily |
| Require Erosion Control and Re-vegetation Plans prior to new developments one acre in size or larger. Inform what the requirements and options are. | 1 yr 1 yr | Establish a guideline or example of a control plan Establish minimum requirements that address appropriate issues | $650/year $650/year | Clay Bodily |
| Include the following erosion protection measures in the information handed out when seeking a building permit: silt fence, straw bales, earth berm for runoff diversion and road watering to minimize dust during road construction | 1-5 yr | Update information | $250/year | Clay Bodily |
| Monitor compliance with building inspector and establish procedures for inspections and train employees (Consider using an Inter-Local Training Meeting.) | 1 yr 1-5 yr 1-5 yr | Establish procedures (written form) Have one employee training meeting Inspect construction sites larger than one acre on a monthly basis. File a report on the findings. Take steps to ensure corrective action. Monitor all construction sites for mud, dust, etc. | $300/year $250/year $2400 | Clay Bodily |

| Post Construction Runoff Control |
| --- |
| MANAGEMENT PLAN | MEASURABLE GOAL | COST | CONTACT PERSON |
| Adopt ordinance setting minimum requirements for landscaping and requiring landscaping on all residential and commercial developments. Set requirements for open spaces, detention ponds, and alternate cul-de-sac turnarounds | 1 yr 2 yr | Review in steering committee Review and pass by city council | $350 $500 | Planning & Zoning Committee |
| Have a storm water drainage system for 1000 E from 50 S to 200 N that drains into a detention pond on Birch Creek Golf Course | 2 yr | Completed system | $40,000 | Clay Bodily Or Jim Gass |
| Develop a procedure to gain approval from the irrigation companies for storm water discharge | 1-5 yr | See Measurable Goal in Illicit Discharge Detection and Elimination Section |  |  |

| Pollution Prevention / Good Housekeeping |
| --- |
| MANAGEMENT PLAN | MEASURABLE GOAL | COST | CONTACT PERSON |
| Establish schedule for maintenance activities including parking lot cleaning, street sweeping, catch basins, curb and gutter cleaning. | 1-5 yr | Have a written policy and schedule to refer to | $2,500 | Clay Bodily or Lyle Izat |
| Offer in-house training to city employees to promote a clear understanding of the impacts of various activities to storm water and promote employee ownership of the problems and the solutions. (Consider using an Inter-Local Training Meeting) | 1 yr 2-5 yr | Obtain information Instigate employee training meeting | $600 | Doug Petersen |

APPENDIX A

BMP FACT SHEETS

APPENDIX B

STORM WATER SYSTEM MAPPING

APPENDIX C

NOTICE OF INTENT

APPENDIX D

CURRENT EDUCATIONAL RESOURCES

| Current Educational Resources |
| --- |
| Title | Publisher | Summary | Storm water topic area |
| Recycle Ferrous Metal & Aluminum | Logan City Landfill & Recycling Center | Tri-fold brochure describing advantages of recycling | Waste reduction reduces possibilities of storm water contamination |
| Recycle Used Oil | Logan City Landfill & Recycling Center | Tri-fold brochure describing the benefits of recycling as well as collection locations | Proper disposal of oil or recycling keeps it out of storm water |
| Recycle Clear Glass Bottles | Logan City Landfill & Recycling Center | Tri-fold brochure describing what types of glass may be recycled and the advantages | Waste reduction reduces possibilities of storm water contamination |
| Recycle Plastics | Logan City Landfill & Recycling Center | Tri-fold brochure describing the advantages of recycling plastic and where it is collected | Waste reduction reduces possibilities of storm water contamination |
| Recycle Used Tires | Logan City Landfill & Recycling Center | Tri-fold brochure describing proper disposal of tires | Waste reduction reduces possibilities of storm water contamination |
| What You Need To Know About Recycling | Cache Valley Clean Team | Tri-fold brochure describing do’s and don’ts for recycling various materials and locations for drop off. (available in Spanish) | Waste reduction reduces possibilities of storm water contamination |
| Curbside Green Waste Collection | Cache Valley Clean Team | Tri-fold brochure describing a curbside collection program recently initiated | Waste reduction reduces possibilities of storm water contamination |
| Hazardous Waste in Your Home | Logan City Environmental Division | Tri-fold brochure describing hazardous wastes and a product disposal guide. Announces a hazardous waste disposal day. | Proper disposal of hazardous waste keeps it out of storm water |
| How to Prepare Materials | The Cache Recycling Coalition | Tri-fold brochure describing how to prepare materials for recycling and listing locations for drop off | Waste reduction reduces possibilities of storm water contamination |
| Cache County Green Waste Facility | Cache Valley Clean Team | Tri-fold brochure describing how to recycle green waste and products available at facility. | Waste reduction reduces possibilities of storm water contamination |
| Recycling Education Program | Environmental Division, Permits and Analysis | Flyer mailers, newspaper and radio ads, manned information booths, flyers at neighborhood councils. | Waste reduction reduces possibilities of storm water contamination. |
| Website Information | Environmental Division, Permits and Analysis | Provide recycling and reuse on the Logan City Website. | Waste reduction reduces possibilities of storm water contamination. |
| Fifth Grade Education | Environmental Division, Permits and Analysis | Visit 80% of the fifth grade classrooms in Logan School district each year | Educating young students establishes a foundation of civic consciousness that they take into their homes. |